## Slide 1: Detection User Manual 2018
AMC Dr. Huang’s Lab
Zhenhuan(Neyo) Yang

## Slide 2: Introduction
This user manual is dedicated for whom use the program Detection.exe.
Detection.exe is a windows-only software designed to perform seizure detection on EEG (electroencephalogram) signals of laboratorial mice.
The rest of the manual includes step-by-step details on the usage of Detection.exe

## Slide 3: Step 1: Export data from Datawave
Open your .ddf file in Datawave
At the bottom left, expand [workspace], expand [project], expand [.ddf], expand [Digital Filter]
On [Filter], right click and select [Save As]
Note: to create digital filtering, please consult lab members.

## Slide 4: Step 1: Export data from Datawave

## Slide 5: Step 1: Export data from Datawave
On [Save as type], select [Text Files]
On [File name], change the file name from *.txt to your own name .txt
Note: it is vital to keep the extension .txt
Change the path to your destination and click [Save]

## Slide 6: Step 1: Export data from Datawave

## Slide 7: Step 1: Export data from Datawave
On [Delimiters], select [Comma]
On [Write Data In], select [Columns]
On [Format], uncheck all the options and do not click on [Skip]
Click [Save]

## Slide 8: Step 1: Export data from Datawave

## Slide 9: Step1.5: Split large data file
Note: For data file which records longer than 1 day, you need to split the data file by day
Click [Start]
On [search] type ‘cmd’
Click on [cmd]

## Slide 10: Step1.5: Split large data file

## Slide 11: Step1.5: Split large data file
Type ‘split –l 86400 [path and name].txt’
Press Enter
Note: output files will be in the directory named xaa.txt, xab.txt …Those are ordered by date

## Slide 12: Step1.5: Split large data file

## Slide 13: Step2: Create labels for channels
Create/Open a new .txt file
Write down the labels for each channel as the same order in the Datawave
Note: It is crucial to separate each label by comma!
Note: If the labels are not given or not as the same number as in Datawave, the program is ging to auto generate label ‘Channel 0’, ‘Channel 1’, ‘Channel 2’…

## Slide 14: Step2: Create labels for channels

## Slide 15: Step3: Open the software
On desktop double click Detection.exe or go to C:\Users\Huang\PycharmProjects\GUI\dist
Note: The program needs some time to initialize
Note: On the bottom right corner, message shows ‘click import to start…’

## Slide 16: Step3: Open the software

## Slide 17: Step4: Select data file
Click [Select Data]
Direct to your data directory, select the .txt file exported from Datawave
Click [Open]
Note: After select the data file, message on bottom right corner change to ‘Data selected!’

## Slide 18: Step4: Select data file

## Slide 19: Step5: Select label file
Click [Select Labels]
Direct to your label directory, select the .txt file created by yourself
Click [Open]
Note: After select the label file, message will change to ‘Labels selected!’

## Slide 20: Step5: Select label file

## Slide 21: Step6: Run the program
Click [Run]
Note: The program needs time to process(e.g. for 1 day 16 channels data, it needs approximately 1 hour). Do not close or click on the program while it’s running!
Note: After the process finished, message will change to ‘Done!’

## Slide 22: Step6: Run the program

## Slide 23: Step7: Save the result
After the process finished, click [Save]
Note: the result will be save to C:\Users\Huang\PycharmProjects\GUI\dist
Note: the result are .pdf of figures. Each file is named after the corresponding label.

## Slide 24: Step7: Save the result

## Slide 25: Thank you!